## Slide 1: iSnooze
Apple
EE459, Spring 2008
Senior Design Project
Engineers: Tony Chen, Nate Houk, Ashwin Sathe

## Slide 2: Objective
Simple
  No feature creep
“It Just Works”™
  No user manual
  Intuitive
Beautiful
  Sleek and hip
  Doesn’t look “cheap”

## Slide 3: Features
“Think Different”™
  Button less
  Seamless iPod integration
  Simple user interface
Standard Features
  Snooze
  Alarm buzzer
  12/24 Hour
  Battery backup

## Slide 4: Schematic
uC
iPod Dock
Touch
Buttons
12:59
Register
Encoder
Register
Register
Register
Data Bus
Address
Input Bus
BCD Drivers
RTC
EEPROM
Beep
Serial
Sun
Mon
Tue
Wed
Thu
Fri
Sat
Bat
Buzz
I2C

## Slide 5: Touch Sensitive Buttons
QTouch Technology
  Key design feature in iPod, iPhone
  Allows us to design a sleek clock housing
QT110 1-Channel
  Detects change in capacitance as a finger approaches the electrode
QT1103 10-Channel
  QFN Package
  Adjacent Key Suppression
Problems
  Soldering
  Tactile Feedback
  Routing of wires causes unwanted capacitance

## Slide 6: iPod Integration

## Slide 7: iPod Integration
Apple Accessory Protocol
  Reverse Engineered
  Poor documentation
  Difficult to obtain parts
  Difficult to obtain robustness
Serial Communication
  Accessory Indicator Resistor
  Command Packets
    Header
    Length
    Mode
    Checksum = [0x100 - (length + mode + command)]
Problems
  Soldering
Increase Volume Packet
sci_write(FF) ;
sci_write(55);
sci_write(03);
sci_write(02);
sci_write(00);
sci_write(02);
sci_write(F9);
// header
// length
// mode
// command
// checksum

## Slide 8: iPod Integration
uC Serial TxD

## Slide 9: Demo

## Slide 10: Problems
Backlight
  Dead on arrival
LCD Fades
  BCD Driver chips unable to sink enough current
iPod Integration
  Not able to fully utilize protocol
Audio Amplification
  Feedback in op-amp circuit caused audio distortion

## Slide 11: Cost Analysis
Part # | Description | Qty | Bulk Price | Total
MC908JL16CPE | uC | 1 | $2.19 | $2.19
VI-319-DP-FC-S | 7-Segment LCD | 1 | $6.80 | $6.80
KIT-LED-41 | LCD Backlight | 1 | $3.25 | $3.25
LEDs |  | 14 | $0.27 | $3.78
74LS374N | Register | 4 | $0.45 | $1.80
74LS247 | BCD Converter | 4 | $0.96 | $3.84
74LS08N | Hex AND Gate | 1 | $0.32 | $0.32
74LS138N | 3-8 Decoder | 1 | $0.41 | $0.41
74LS148N | 8-3 Encoder | 2 | $0.80 | $0.80
DS1307 | RTC | 1 | $1.69 | $1.69
24LC256 | EEPROM 256k | 1 | $1.35 | $1.35
DS32KHZ | Oscillator | 1 | $2.55 | $2.55
10Mhz | Oscillator | 1 | $1.27 | $1.27
QT1103 |  | 1 | $2.17 | $2.17
Resistors Pack | 330Ω, 1Ω , 2Ω, 10KΩ , 500KΩ | 6 | $.31 | $1.86

## Slide 12: Cost Analysis
Part # | Description | Qty | Bulk Price | Total
Capacitors | 100pF, .1uF | 20 | $0.10 | $2.00
3.3v Battery |  | 1 | $0.85 | $0.85
Speakers |  | 2 | $1.59 | $3.18
Buzzer |  | 1 | $0.50 | $0.50
Piezo Speaker |  | 1 | $0.50 | $0.50
iPod Dock Adaptor |  | 1 | $0.50 | $0.50
AC Adaptor |  | 1 | $4.35 | $4.35
 |  |  | Total | $45.96
 | Apple Volume Discount 20% |  |  | -$9.19
 |  |  | Cost Basis | $36.77
 |  |  | Price Point | $49.99
 |  |  | Profit | $13.22
 |  |  | Profit Margin | 26.4%

## Slide 13: Questions?